88888888888888888888888                            JCPDS-NBS*LSQ82
               A Least Squares Unit Cell Refinement Program

                           Camden R. Hubbard
                       Inorganic Materials Division
    		       Center for Materials Science
    		       National Bureau of Standards
    		          Washington, D.C.   20234

                                   and
                       Steven M. Lederman and Nikos P. Pyrros
                 JCPDS--International Centre for Diffraction Data
                             1601 Park Lane
                          Swarthmore, PA   19081
  
                                  -1-

                          
                          TABLE OF CONTENTS

PREFACE..........................................................ii   

AVAILABLE COMPUTER PROGRAMS FOR X-RAY POWDER DIFFRACTION.........iii

INTRODUCTION.....................................................1

PROGRAM DETAILS..................................................3

    Quantity Minimized...........................................3

    Figures of Merit.............................................3

    Systematic Error Test........................................5

    Auto Indexing................................................6

    Data Rejection...............................................7

PROGRAM EXECUTION

    Batch Mode...................................................8
   
    Batch Mode Input Card Descriptions and Formats..............10

    Interactive Mode............................................17

    Interactive Mode Input Description..........................18

    PKS File Mode...............................................20

DEFAULTS........................................................21       
                                                                         
EXECUTION ON NBS' UNIVAC 1182...................................22       
                                                                         
REFERNCES.......................................................23

APPENDICES

    A.   D-Spacing Generation Example
 
    B.   Least-Squares Example

    C.   PKS File Input Example

    D.   PKS File Format

                                   i

                                PREFACE

    The computer program, JCPDS-NBS*LSQ82, was developed as part of the
cooperative program in x-ray powder diffraction between the JCPDS--
International Centre for Diffraction Data and the National Bureau of
Standards.  In addition to computer program development, outputs of the
cooperative program include high quality x-ray powder diffraction
refernce patterns, editorial review of data entering the Powder 
Diffraction file (PDF), and critical evaluation of the current contents
of the PDF.  The JCPDS--International Centre for Diffraction Data 
publishes the PDF, search indexes, selected subfiles, and related items.

    For details of publications by the JCPDS--International Centre for
Diffraction Data, write to:

           General Manager
           JCPDS--International Centre for
           Diffraction Data
           1601 Park Lane
           Swarthmore, PA   19081

    Other computer programs available at NBS for x-ray powder
diffraction are listed below.  Related publications and/or 
program listings will be sent upon request.  For details, 
write to:
                                                                               
    	   Dr. Camden R. Hubbard
    	   A221/Matls
    	   National Bureau of Standards
    	   Washington, D.C.   20234

For a copy on magnetic tape, send a separate reel for each program
package (9-track, 1600 bpi, labeled).  The tape will be written in
ASC11 with multiple records per block.  Univac users may request 
Copy, G format of symbolics, relocatables, and absolutes.  In all
cases, necessary data files and test decks are included.  All
programs are written in FORTRAN77 and are running on a Univac 1100
computer.

                            iii

    AVAILABLE COMPUTER PROGRAMS FOR X-RAY POWDER DIFFRACTION
 
JCPDS-NBS*POWDER82.  (N.P. Pyrros and C.R. Hubbard)  This 
package of programs is used to analyze digitally collected
powder patterns.  It includes background determination, second 
derivative peak location, external standard 2 calibration, PKS
file creation and editing, as well as several plotting routines. 
The PKS file provides tthe connectivity between modules and the
least-squares program, JCPDS-NBS*LSQ82.

NBS*QUAN82.  (C.R. Hubbard and R.L. Snyder) A package of programs
for general quantitive analysis by spiking, intensity ratio, or
internal standard methods.  Measurements of multiple lines and
multiple mountings can be used.  In the internal standard method,
overlapped lines and elemental analysis data can be included to
improve the XRD phase analysis.

AUTO.  (R.L. Snyder, C.R. Hubbard, and N.P. Pyrros) AUTO is an
interrupt driven, dual diffractometer control program.  It
permits collection of data for an entire pattern or from 
selected regions.  The raw data file can be read directly by 
JCPDS-NBS*POWDER82 and NBS*QUANT82.
NBS*AIDS83.  (C.R. Hubbard, J.K. Stalik,A.D. Mighell, and
M. Holomany)  This is a revision of NBS*AIDS80 for single
crystal and powder diffraction data evaluation, crystal data
cell calculation, hke/20/d-spacing generation, numerous data
consistency checks, least-squares refinement of lattice 
parameters (subset of LSQ82), and figure-of-merit calculations.

            
                        JCPDS-NBS*LSQ82
             A least Squares Unit Cell Refinement Program

                        INTRODUCTION

    The determination of lattice parameters from x-ray powder
diffraction data is an important step in the characteization
of a crystalline phase.  X-ray powder diffraction data can
lead to cell parameters accurate to a few parts in 10,000 or
better (e.g., see NBS Monograph 25, Section 19, 1982).  Such
accuracy is achieved with measurement of peak locations to
within 0.01 20, internal standard calibration of 20, and,
finally, a least-squares refinement of unit cell parameters.
For nearly twenty years, the program of Evan's Appleman and
Hardworker (1973) has been widely used for this purpose.
There program is commonly referred to as the Geological
Survey program.  This report describes a new version of the 
program which includes conversion to FORTRAN77 and major
revision of the program's input and output features.  Only
minor, special case revisions to their computational
segments were required.

    The new program, JCPDS-NBS*LSQ82, provides for three
alternative modes of data input:  prompted free format 
interactive input; formatted card image input; and reading 
of a magnetic data file created by the JCPDS-NBS*LSQ82 
system of programs (Pyrros and Hubbard, 1983).  The input
data are checked for consistency with the program 
requirements.  Extinction conditions can be automatically
generated from the space group, aspect or centering
symbol.  In the formatted card image input mode, the unit
cell angles can be entered either as degrees in decimal
form or as degrees and minutes in integer form.  To
allow for reduction of printed output, often needed in
interactive computing, print options have been added.  
The final listing was reduced in length by up to 50 
percent and made more reliable by printing the author's d, 20,
and hk data on the same line as the program's generated d', 
20', andh'k'e', when equivalent.  The calculation of figures
of merit by two methods has been added to enable the user to
evaluate the quality of the derived unit cell and the internal
consistency of the cell and observed data, respectively.
Several tests for the presence of systematic errors have also
been added.  These include the average of 2* calc 2* obs'
comparison of the number of lines with * greater than and
less than 0.02, and a statistical test for nonrandomness in
2* as a function of 2* (Hubbard and Stalick, 1982).

    JCPDS-NBS*LSQ82 meets the requirements of ANSI standard
FORTRAN77.  The dimensions of large arrays can be readily 
changed by revising the appropriate FORTRAN PARAMETER
statements in each routine.  As distributed, the maximum
number of observed lines (MAXOBS), the maximum number
of program generated lines (MAXGEN), and the maximum 
number of lines in the peak file (MAXPKS) are set at 200,
1000 and 300, respectively.  With these array dimensions, the
code requires ???? words for data storage and ???? words for
program instruction on the UNIVAC 1100/82 (one word=36 bits).
Overlaying could reduce the storage required for program
instructions but would probably save little data storage.

    The authors wish to acknowledge the helpful suggestions of
J. Stalick, E. Evans, H McMurdie, M. Morris, B. Paretzkin,
and B. Post.

                          -2-

                       
                        PROGRAM DETAILS 

Quantity Minimized
     The Geological Survey program minimizes,



where *corr/hkl is the observed value of theta corrected for
instrumental and physical peak shifts (e.g., L* effects,
sample displacement, film shrinkage), *calc/hkl is the theta
value calculated from the current unit cell parameters, and
w/hkl is a weighting factor.  The corrections are readily 
determined through use of 2* internal standard.  Since they
unit cell parameters are related nonlinearly with *calc, a
nonlinear least-squares refinement is used.  The Evans, Appleman,
and Handwerker (1973) paper fully describes details and 
determination of the estimated standard deviations of the unit
cell parameters.
           
Figures-of-Merit

    Both M20 (de Wolff, 1968) and FN (Smith and Snyder, 1979) 
figures-of-Merit are calculated by the program.  M20 is defined
by, 




where Q=1/d2, Q20 is the value of Q for the 20th observed line (not
counting unexplained lines), N20 is the number of different calculated Q
values up to Q20, and is the average magnitude of the discrepancy in Q
for these 20 lines.  The number of unindexable lines occurring, up to
the 20th observed and indexed line, is X20.  A value of M20 10 will
guarantee the essential correctness of the indexing provided these are
not more than two spurious lines (X20<2) [de Wolff, 1968].

    FN is defined by,




Where n is 30, or the maximum number of lines of the pattern if the
entire pattern has fewer than 30 lines. Nposs is the number of 
diffraction lines allowed in the space group, up to the nth observed
and indexed line.  Co-positional lines, such as the cubic 221 and 300,
are counted as on possible line. HKL is the average absolute magnitude
of the difference between the corrected and calculated 20 values for
each reported hkl for the first N lines.  FN thus indicates the 
accuracy and completeness of the data.  The format for reporting the
Smith-Snyder figures of merit is FN(  ,Nposs).  Values reported in
NBS Monograph 25, section 18, range from F30= 17.6(0.017,99) toF10=
121.6(0.008,10).

    If the user assigns two sets of indices to a single observed line
(multiply indexed line), then the equations for M20 and FN can be 
implemented in two ways.  One can choose the set with smaller*20
and ignore the other set.  Alternately, both  *hkl and *hkl can
be included in the average.  The latter approach was chosen for
NBS*AIDS80 (Mighell, Hubbard, and Stalik, 1980) and implemented in
JCPDS-NBS*LSQ82.  This yields a lower figure-of-merit when two or
more hkl values are assigned to a *corr value  Another problem
which involves determination of Nposs can lead to different values
of M20 and Fn depending on program implementation.  The definition of
Nposs is the number of space group allowed lines out to *N.  To
allow for the possibility that *calc hkl>n hkl and than nposs then
would not include the calculated line hkl requires to index *N hkl
an increment of 0.025 is added to N prior to counting Nposs.

Systematic Error Tests

    The possiblity os systematic errors in 20 corr is tested in three
ways:  (1) average*20 (=20 corr -20 calc); (2) number of lines with                                     	                    
*20 greater than +0.02 and less than -0.02; and  (3) a statistical
test.  All three tests use only the lines indexed at the end of the
final d/hkl/20 table.  If given an input line was assigned multiple
sets of hkl, then the *20 for each hkl is used just as in the 
calculationof figures-of-merit.

    The statistical test is based upon the paper, "On Randomness in
Ordered sequences", by young (1941).  He shows that when,






and,





then, statistically, the *20 ordered sequence of *20 values is not
randomat the 95 percent significance level if c/o > 1.645 and at
the 99 percent level if c/0>2.326.  To apply Young's equation to
the *20 ordered sequence of *20 differences, let,



and


In the powder diffraction case, when**i/n=* is non-zero, systematic
errors are likely.  For least-squares refined cell parameters, * is
essentially zero.  Thus, we have refined c to be,
                                                  




so that *c/o will be larger when * is non-zero.  One drawback of the
*c/o test is that it is quite sensative to inclusion of a misindexed
line (large****).  It also can give an indication that systematic
errors are present in the data when all ** are small and the sequence
of * values is not important.

Auto Indexing

    Often a user will have a trial cell and a set of corrected *20
values.  The program can be used to assign sets of *hkl to the *20
values.  This is often called Auto Indexing.  Because lower *20 
reflections can be assigned *hkl sets more easily than at higher
*20, the program only assigns sets of *hkl for reflections below
THTMX for the first NCYC cycles of cell parameter refinement.  All
reflections index  will have *20 less than TOL is initially set to
TOLMX.  TOL is automatically adjusted after each cycle to two times
the standard error of a unit weight observation for TOLMN, which 
ever is larger.  After the NCYC cycles, the program attempts to
index all reflections.  If a reflection cannot be indexed with *20
<TOL, then it remains unindexed.

    Auto indexed reflections do not contribute to the least-squares
equations if the indexing choice is not unique.  Such cases are
flagged with an 'M' in the final llisting (See test B1) when (a)
the observed *20 is within TOL of the generated *20; (b) a second 
generated *20 corresponding to the auto indexed line; or (c) two
observed *20 are within TOL of each other.

Data Rejecrion

    User indexed reflections will not contribute to the least-squares
equations if the *20 exceeds TOL.  These refections
are flagged with an 'R' (*e.g.,in test 01, the )  the 1 2 2 at 34.770
has *20 =0.046, while TOL on the final cycle is 0.040).  Reflections 
which are obviously misindexed on input  (**20>0.3deg.), as compared
to the generated *20 based on the input lattice parameters, are set
to unindexed (*hkl flag U).  The program will attempt to assign a 
new set of hkl, as discussed above under Auto Indexing.  When this case 
occurs, a "BAD HKL" message is printed. If an input set of hkl; are 
not allowed by the systematic extinctions, the hkl flag is set to "U",
and then the reflection is considered unindexed.  Such lines may be
assigned an hkl set by the auto indexing feature.

                           -8-
                         PROGRAM EXECUTION

    Three modes of data input are allowed by JCPDS*LSQ82:  batch,
interactive, and PKS file input.  Upon initiation of the program,
the prompt message, "ENTER:  TITLE, DEMAND, PKFILE, OR FINISH"
allows selection of input mode.  TITLE would signal that the input
is to be formatted by card images (usually used for batch mode
execution).  DEMAND would signal that free formatted input is to
be used  (usually for interactive use).  PKFILE would indicate
that a PKS file created by the powder pattern analysis package
JCPDS-NBS*POWDER82 is to be read.  Multiple problems can be run
one after the other.  FINISH terminates all input.

    Details of the input data for each of the three modes are
given in the following three sections.

Batch Mode

    The input of data via card images with formatted fields for 
each possible input parameter was the only input mode allowed by
the original Geological Survey program.  This type of input is
often referred to as "batch" input and typically involves punched
cards.  Two additions to the batch mode input are of particular
importance.  First, lattice parameters are input on either a
"PARAM" or "PARAMD" card type.  The former requires angles in 
degrees and minutes integer form, while the latter requires
degrees in decimal form.  The second modification was to allow
space group, aspect or centering symbol input via a SPACEG 
card to simlify entering hkl* extinction condition information.
Input of the extinction condition information is still possible 
on a SYSEXT card.   Only one of each pair ( PARAMD or PARAM
SPACEG or SYSEXT) should be included for each problem.  The
card formats are described in detail in the next section.
                         end -9-


                            -10-

Batch Mode Input Card Descriptions and Formats

Type of        Column     Format      Variable  Description	     
Card           Nos.        

TITLE          1-6        A-6         ITEST     The word TITLE
                                                  with column 6
                                                  blank.
               
               7-80       A74         IHEAD     Any alphanumeric
                                                    information de-
                                                  sired in heading.

PARAMD or                                       **Note only the
PARAM                                           unique lattice
                                                parameters should
                                                be entered.
                                                
                                                System unique parameters
                                                CUBIC  a
                                                TETRA  a and c
                                                ORTHO  a,b, and c
                                                MONOC  a,b,c, and beta
                                                RHOMB  a and alpha
                                                HEXAG  a and c
                                                HEXAR  a and c

PARAMD         1-6        A6          ITEST     The word PARMD

               7-15       F9.6        AO(1)     Unit cell length a

               16-24      F9.6        AO(2)     Unit cell length b

               25-33      F9.6        AO(3)     Unit cell length c

               34-41      F8.3        ALO(1)    Angle alpha in degrees

               42-49      F8.3        ALO(2)    Angle beta in degrees

               50-57      F8.3        ALO(3)    Angle gamma in degrees

               58         II          ITTH      Flag for data input
                                                =1 for theta
                                                =2 for 2-theta

               59-61      F3.0        THTMX     Angle limit in degrees
                 				used for first NCYC 
    						cycles for indexing
    						observations (default
    					        =40 degrees 2-theta).

               62         II          NCYC      Number of cycles during
    						which non-indexed 
    						reflections with angles
    						exceeding THTMX are
    						not accepted in least-
    						squares solution.  If
    						NCYC is given as zero or
    						blank, a default value
    						of 2 is assigned by the
    						program.

            63-67      	F5.4        TOLMN       Minimum tolerance used
    						in accepting reflections
    				                (Default =0.03 in 
                                                 2-theta). 
            68-72       F5.4        TOLMX       Starting tolerance used
    						in accepting reflections
    						(Default =5.0*TOLMN)

            73          IT          IPHKL       Flag for print control:
    						=0 for print everything
    						=1 for do not print re-
    						flection data for each
    						cycle (i.e., print only
    						a summary following each
    						cycle).

           74          	IT          IXPD        Flag for final table
    					        printing:
    						0=for print
    						=1 for do not print

          75            IT          NOINDX      Flag for use of input
    						hkl indexes:
    						0=use each hkl set input
    						1=consider every line
    						unindexed

         76-80          F5.3        RESOLV      2-theta difference 
    					        between two generated
    						lines in order to be
    						considered resolved
    						(Default =0.075 in
    						2-theta)

		 		 			                                                                           
Type of    Column     Format      Variable    Description
Card        Nos.

PARAM      1-6        A6          ITEST       The word PARAM (alter-
    					      nate format to PARAMD
    					      input)

           7-15       F9.6        AO(1)       Unit cell length a

           16-24      F9.6        AO(2)       Unit cell length b

           25-33      F9.6        AO(3)       Unit cell length c

           34-36      I3          IDG(1)      The number of degrees
    					      in the angle alpha



           37-41      F5.3        FMN(1)      The number of minutes
                                              in the angle alpha
           

           42-44      I3          IDG(2)      The number of degrees in
                                              the angle beta
                               
           45-49      F5.3        FMN(2)      The number of minutes in
                                              the angle beta                                          		              
			 
                  
           50-52      I3          IDG(3)      The number of degrees in                                                                                                         
                                              the angle gamma


           53-57      F5.3        FMN(3)      The number of minutes in
                                              the angle gamma


           58-79                              See instructions for
                                              PARAMD


SPACEG    1-6    A6     ITEST    The word SPACEG
          7-11   A5     ICRYST   Choose one of the following:
                                 CUBIC, TETRA, ORTHO, MONOC,
                                 RHOMB, TRICL, HEXAG, OR 
                                 HEXAR
                                 NOTE: HEXAR must be used for 
                                 rhombohedral lattice on hex-
                                 agonal axes.

                                              
          12-14  F3.0   THEMX    Limit of 2-theta for generating
                                 hkl.  Defaults are:  (1) 179 deg. 
                                 for hkl  generation; (2) maximum
                                 2-theta observed +0.5 deg. for
                                 least-squares refinement.
                                                                        


                
   Type of     Column    Format    Variable      Description
   Card        Nos.
               15-20     F6.5      PWL           Alternate field for 
                                                 lamba retained for
                                                 compatibility with
                                                 old desks.  See
                                                 columns 50-80.)

              21-22      2x                      Blank

              23-30      8A1      ISGI           Space group, aspect,
                                                 or centerin symbol
                                                 (e.g., P21/a or Fm3m).
                                                 The systematic extic-
                                                 tions automatically
                                                  generated from the
                                                   symbol.  The allowed
           
              31-49      19x                     Blank

              50-60      F11.6     PWL2          Primary field for 
                                                 Lambda.  If>0, this 
                                                 value is used no
                                                 matter what is in 
           					 columns 15-20.  If
    						 both 15-20 and 50-
    						 60 are left blank,
    						 then the default
    					         value, 1.5405981 A,
    						 is used.


               				                                                                                 
              61-62     I2     IWTYP             =0 for use input 
                                                 weights   =1 for
                                                 use unit weights
                                                 =2 for use Hess'
    						 weights (Hess', 1951)

              63-64     I2     IWCYC             Number of cycles to
    						 use weights before
    						 all are reset to 1.0.
    						 A zero implies use of
    						 weights according to
    						 IWTYP for all cycles

              65-80    	16x                      Blank


Type of    Column     Format     Variable    Description
Card       Nos.      
SYSEXT     1-6        A6         ITEST       The Word SYSEXT
(alter-
nate for
SPACEG)    7-14                              See instructions for
                                             SPACEG card

          21-47       IOP(1) to IOP(47)      In any column, enter the
                      inclusive              specific value for B (2,3,
                                             4, or 6) which satisfies
                                             the reflection condition
                                             assigned to that column

                                             Class of  Conditions for
                                             Reflec.   Non-extinction
                                                                                                                                
          21          I1                       hkl     h+k=Bn
          22          I1                       hkl     h+l=Bn
          23          I1                       hkl     h+l=Bn
          24          I1                       hkl     h+k=Bx, h+l=By,
                                                       k+l=Bz (x,y,z
                                                       are any integers)
          25          I1                       hkl     h+k+l=Bn
          26          I1                       hkl     -h+k+l=Bn
          27          I1                       hhl     h=Bn
          28          I1                       hhl     l=Bn
          29          I1                       hhl     h+l=Bn
          30          I1                       hhl     2h+l=Bn
          31          I1                       Okl     K=Bn
          32          I1                       Okl     l=Bn
          33          I1                       Okl     k+l=Bn
          34          I1                       hOl     h=Bn
          35          I1                       hOl     l=Bn
          36          I1                       hOl     h+l=Bn
                   
                                  -14-

   Type of     Column     Format     Variable   Description
   Card        Nos.

                                                Class of  Conditions for
                                                Reflec.   Non-exticntion

               37         I1                    hkO       h=Bn  
               38         I1                    hkO       K=Bn
               39         I1                    hkO       h=k=Bn
               40         I1                    hhO       h=Bn
               41         I1                    hOO       h=Bn
               42         I1                    OkO       k=Bn
               43         I1                    OOl       l=Bn
               44         I1                    hll       h=Bn
               45         I1                    hll       l=Bn
               46         I1                    hll       h+l=Bn
               47         I1                    hll       h+2l=Bn
               48-49      2x                    Blank     
               50-72                            See instructions for
                                                SPACEG card


REFLECTION     1-3        A3                    Blank or HKL
               4-6        3x                    Blank
               7-11       15     IH(I,1)        h index (see below)
              12-16       15     IH(I,2)        k index (see below)
              17-21       15     IH(I,3)        l index (see below)




   Type of     Column     Format      Variable  Description
   Card        Nos.

                                                NOTE: h, k, and l are
                                                optional on any 2-theta
                                                card.  If left blank,
                                                computer will attempt to                  	                                                      
                                                assign hkl's.  User              
                                                assigned hkl remain            
	                                        fixed for all least-             
                                                squares cycles.

                                                       
                                                     
               22-30      F9.6        DSP(I)    d-spacings*
               31-38      F8.6        WL(I)     Alternate lambda--
                                                used to override                                     
                                                value on SYSEXT 
                                                card or default value.         
                                                Thus one can leave a
                                                blank here for k*a2
                                                here for specific re-
                                                flections.  Non-zero
                                                WL applies only to the
                                                card on which it is
                                                entered.

                  
       
               39-47      F9.5        OBSTH(1)  The bragg angle 2-theta
                                                in decimal degrees*

                                                                                   
   END         1-3        A6          ITEST     The word END with blanks                                                            
                                                in columns 4, 5, and 6.
                                                Indicates end of a prob-
                                                lem.  A new problem may
                                                follow.

   FINISH      1-6        A6          ITEST     The word FINISH. This
                                                card is used only once,
                                                after the END card of 
                                                the  last problem.  It 
                                                is the signal that there
                                                are no more problems.

*Enter either d-spacing or Bragg angle 2-theta, but not both for the
 same reflection.


 Interactive Mode

     Control parameter and data input via an interactive terminal is

 also provided by the program upon entering the responce DEMAND. 

 In this mode, the program uses free format input.  That is, if a 
 
 list of items is requested, the user enters the items separated by

 a comma or a blank.  To accept the default value, a slash ("/") is

 entered.  Each user input is prompted by the program.  The meaning

 of each particular variable was defined under the section, BATCH

 MODE INPUT DESCRIPTIONS AND FORMATS.  This mode is frequently used 

 to generate a listing of possible 2*'s for a known cell and space

 group (often referred to as "d-gen").  After entering the crystal 

 system, only the unique initial lattice parameters are requested.


Interactive Mode Input Description

All numerical inputs are free format.  Separate numbers in a list
by a space or comma.  A "/" is used to skip entry and accept de-
fault values.

   Prompt Message          Variable   Responce

   ENTER: TITLE, DEMAND    ITEST      DEMAND
   PKF FILE, or FINISH

   ENTER HEADINGS (A68)    IHEAD      Any alphanumeric title information
                                      --68 characters
   
   ENTER CRYSDTAL SYSTEM    ICRYST     CUBIC, TETRA, ORTHO, MONOC,
   CODE (A5)                           RHOMB, TRICI, HEXAG, HEXAR

   ENTER a (free format)    AO(1)      Unit cell length a

   ENTER b*                 AO(2)      Unit cell length b

   ENTER c*                 AO(3)      Unit cell length c

   ENTER alpha*             ALO(1)     Unit cell angle alpha

   ENTER beta*              ALO(2)     Unit cell angle beta

   ENTER gamma*             ALO(3)     Unit cell angle gamma

ENTER PARAMETER INPUT FLAG  ITYPE      1 for theta
                                       2 for 2-theta
                                       3 for D-spacing

IS A LEAST-SQUARES TO BE        Y for yes
DONE?                           N for no

ENTER: NCYC, THTMX, TOLMN,      See PARAMD card.  A "/" is used
TOLMX, and RESOLV               to accept default values

ENTER:IWTYP, and IWCYC          See SPACEG card.  A "/" is used
                                to accept default values

ENTER: 2-THETA-MAX, IPHKL,      See SPACEG card.  Note that 2-
IXPD, PWL2                      THETA-MAX or THETA MAX is re-
                                quested, based in ITYPE


*Only the unique parameters are requested.




   Prompt Message          Variable    Responce

   ENTER: SPACE GROUP,     SPGI        See NBS TECH Note 1141, Appen-
   ASPECT or CENTERING(A8)             dix A.  First character in upper
                                       case. All other numeric or 
                                       lower case alphabetic (a,b,c,
                                       d,m, or n) 

   ENTER:
   THETA, hkl, WEIGHT, LAMBDA;         Input reflection data.  The
   2-THETA, hkl, WEIGHT, LAMBDA; or    choice of theta, 2-theta, or
   D-SPACING, hkl, WEIGHT, LAMBDA      d-spacing is selected by input                                                                                                                                          
                                       flag ITYPE(see above). A0.0
                                       in the first field terminates
                                       data input. A "/" after any
                                       value is acceptable.  For ex.
                                       to input only the 2-theta value
                                       20.0; enter 20.00/
         


PKS File Mode

     In the PKS file input mode (PKFILE), a computer file created
by the JCPDS-NBS*PATTERN82 system of programs is read.  This file
contains all the parameters (e.g., cell, space group, 20's*, etc.)
needed by JCPDS-NBS*LSQ82.  The reflections in the file are marked
to be used or not to be used in the least-squares refinement.  Re-
flections flagged as "not to be used" are, however, compared with
the final list of possible reflections.  If a possible reflection
and a "not to be used" observation closely fit, this is noted in
the final listing.  This feature permits use of well resolved, strong 
reflections for a preliminary cell parameter refinement.  Then, when
weak peaks are clearly indexed, they can be marked "to be used" in 
least-squares refinement and the program rerun.  An example of this 
program mode is given in Appendix C.  The PKS file format is given
in Appendix D.


                       DEFAULTS

     The following conditions or constants apply for all input modes
unless non-zero values are entered.

1.   If input is in terms of 2-theta, output will also be in 2-theta.
     Input of "d's" is OK; output then is in 2-theta by default.  If
     out put is in theta, output will be in theta; for this option,
     it is necessary to set ITHT=1 on the PARAM or PARAMD card, col. 58,
     format I1.

2.   Lambda= 1.5405981 A.

3.   Reflections greater than 2*=40.0 deg. are not used in the first
     two (NCYC) cycles.

4.   Maximum tolerance at the beginning is 0.15 degrees in terms of 2-
     theta (TOLMX).  Only reflections with 2*obs -2*calc. <0.15 are
     used to refine the cell on the first cycle.

5.   Minimum toerance is 0.03 degrees in terms of 2-theta (TOLMN).

6.   Each reflection is given a weight of 1.0. If other weight are
     assigned on input, they are used for all cycles unless spec-
     ified otherwise (see IWCYC on card SPACEG).

7.   Twice the standard error of an observation of unit weight is used
     to obtain the value of angular tolerance, TOL.  However, TOL is
     bounded by the limits TOLMX and TOLMN.
   

                     EXECUTION ON NBS' UNIVAC 1182

Interactive Mode

1.    Sign on with qualifier, POWDER

2.    Enter:  @XQT POWDER.LSQ82

3.    Enter:  DEMAND

4.    Input data following program prompts

5.    When least-squares is done, enter DEMAND for next problem or
      FINISH to terminate.

Batch Mode--punch cards as follows:

1.    @RUN, M* RUNID Account, project, max time, max pages

2.    @ASG, AX POWDER*POWDER.

3.    @QXT POWDER*POWDER.LSQ82

4.    Data cards for one or more problems--first card has TITLE in
      columns 1-5.

5.    FINISH

6.    @FIN

PKFILE Mode (Interactive)

1.    Sign on with qualifier POWDER

2.    Enter:  @XQT POWDER.LSQ82

3.    Enter:  PKFILE

4.    Enter:  file name following program prompt

5.    Enter:  FINISH


                   REFERENCES

1.  Evans, H.T.,Jr., Appleman, D.E., and Handwerker, D.S. (1973)
    Report #PB216188, U.S. Dept. of Commerce, National Technical
    Information Center, 5285 Port Royal Road., Springfield, VA
    22151.

2.  Hess, Acta Cryst., 4, 209-15 (1951).

3.  Mighell, A.D. Hubbard, C.R., and Stalick, J.K., "NBS*AIDS80:
    A FORTRAN Program for Crystallographic Data Evaluation", NBS
    Technical Note 1141, National Bureau of Standards, Washington
    D.C.   20234

4.  Smith, G.S., and Snyder, R.L. (1979) J. Appl. Cryst., 12, 60.
    
5.  de Wolff, P.M. (1968) J. Appl. Cryst.,1, 108.

6.  Young, L.C. (1941) Annals of Math. Stat., Vol. XII, 3, 293-300.

   
                          APPENDIX A
                   D-Spacing Generation Example

     The test data listed belo show the input required for d-spacing
generation in the interactive mode (DEMAND).  The underlined items are
the required input parameters.


                           APPENDIX B
                    Least-Squares Examples


     The JCPDS--International Centre for Diffraction Data Least-
Squares Task Group has surveyed available least-squares programs,
including this program.  By comparing lattice parameters and 
estimated standard deviations for eleven different test data sets,
they found that most programs yielded the same results.  The 
eleven test data sets and the JCPDS-NBS*LSQ82 least-squares 
refinement results are given below.

     The first seven test decks provide a test for the following
crystal systems:  triclinic, monolinic, orthorhombic, tetragonal,
hexagonal, rhombohedral, and cubic.  In each case unit weights
and assigned hkl were used throughout the least squares require-
ments.  Test deck #8 repeats test deck #2 (monoclinic) using hess'
weighting scheme.  Test deck #9 repeats test deck #3(orthorhombic)
with practical weights.  The practical weights are empirical and 
are 1.0 unless downweighting is appropriate, because: (a) two or
more calculated 20* reflections are within 0.04 20* of the observed 20* 
(b) the observed 20* was subject to possible distortion, due to 
overlap with an adjacent line; or (c) *20 corr was derived by use of 
etrapolated internal standard correction.  Test deck #10 adds random
noise of +0.01, 0.0, and -0.01 20* to the 20* values of test deck #2.
Test deck #11 adds randoms noise (0.01,0.00,-0.01) to the 208 values of 
test deck #3.  For test deck #1, nearly complete output is shown.
For the other ten decks, IPHKL was set to two, so that only a summary
for the last cycle and a final listing were printed.  Only the summary
is included below.  Any one of the eleven test decks can be run letting
the computer assign hkl (setNOINDX=1, col 75 on card PARAMD).  Execut-
ion of test deck #B1 shows typical results.  The small differences in
refined lattice parameters between deck #1 and #B1 are due to the 
exclusion from the least-squares refinement of lines with multiple index
(flag='M') possibilities.  


     Each example is preceeded with a listing of the test deck.  The
first line of the listing gives the test deck number (e.g.,POWDER*
LSQ82.  TESTOL on the next page).  In the example execution, the line
CADD, P LSQ82.TESTOL, for example, indicates the point of data input.